## Slide 1
Running Projects Update
Date (DD/MM/YYYY)

## Slide 2
S. No | Project | Target Structure | G.L Name | Qty | Start Date | End Date | On time | Remarks
1 | A11CF |  | Leader A | 1 kg | 01-06-26 | 04-08-26 | NO | 1 kg COA has been shared along with the 2 g of each sample sent to customer, waiting for customer feed back 10 g of compound was shipped
2 | B4I90 |  | Leader A | 20 g | 09-05-26 | 28-06-26 | NO | 20 g was shipped on 27-08-2026 and ~ 25 g is in hand.
3 | A1TRP |  | Leader B | 20 g | 09-05-26 | 28-06-26 | NO | 20 g was shipped on 27-08-2026 and ~ 25 g is in hand
4 | B0MI2 |  | Leader B | 20 g | 09-05-26 | 28-06-26 | NO | 20 g was shipped on 27-08-2026 and ~ 25 g is in hand
5 | CK05R |  | Leader A | 200 g | 1-04-26 | 02-09-26 | Yes | We have started the working on new scheme and final compound was confirmed.
6 | A2NSQ |  | Leader B | 200 g | 1-04-26 | 02-09-26 | Yes | We are working on final stage, to improve yields.
7 | BG5JD |  | Leader A | 500 g | 28-08-26 | 30-10-26 | Yes | Raw materials were ordered.

## Slide 3
--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Overview:.
1.2 kg of final stage compound was prepared, and COA for 1 kg has been shared.
We have shipped 2 g of stage 1 compound, 2 g stage 2 compound and 2 g of final stage compound.
Waiting for customer feed back on the three samples.
20 g of final stage compound was converted to its free base and got 11.5 g with 96 % purity by HPLC and conformed by HNMR and 10 g sample was shipped.
Project: A11CF
Route of Synthesis

## Slide 4
--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Overview:
45 g of stage 3 compound was prepared and 20 g was shipped on 28-08-2026.
Route of Synthesis
Project: B4I90

## Slide 5
--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Overview:
46 g of stage 6 compound was prepared and 20 g was shipped on 28-08-2026.
Route of Synthesis
Project: A1TRP

## Slide 6
--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Overview:
48 g of stage 5 compound was prepared and 20 g was shipped on 28-08-2026.
Route of Synthesis
Project: B0MI2

## Slide 7
Overview:
50 g of stage 3 compound converted to stage 4, using catalyst adduct and got 45 g, its HPLC showed 95 % purity. (55 % yields)
950 g of stage 3 compound converted to stage 4, using catalyst adduct and got 886 g, its HPLC showed 94 % purity (56 % yields).
886 g of stage 4 compound converted to stage 5 and got 470 g with 97 % purity by HPLC.(57 % yields)
5 g of stage 9 compound was attempted to convert to stage 10 using catalyst, reaction monitored by TLC and isolated got 4.5 g crude solid, its HPLC showed 69 %, along with 26 % non-polar impurity. This was purified by RC using solvent and got 2.2 g with 98.6 % purity by HPLC.
5 g of stage 9 compound was converted to stage 10 using catalyst adduct and got 1.8 g after purification, its HPLC showed 98 % purity.
5 g of stage 9 compound converted to stage 10 using catalyst and got 2.4 g after purification, its HPLC showed 98 %.
5 g of stage 9 compound converted to stage 10 using catalyst and got 2.2 g after purification, its HPLC showed 98 %.
250 g of stage 5 compound converted to stage 7 and obtained 295 g with 98 % purity by HPLC. (80 % yields)
295 g of stage 7 compound converted to stage 8 and got 350 g, its HPLC showed 98 % purity.(90 % yields)
Route of Synthesis
Project: CK05R

## Slide 8
1 Kg of stage 1 compound converted to stage 2 and got 850 g its HPLC showed 96 % purity.
250 g of stage 2 compound converted to stage 3and got 195 g.
25 g of stage 4 compound converted to stage 5 and got 9.8 g after column purification and conformed HNMR (40 % yields).
500 g of stage 2 compound converted to stage 3 and got 383 g with 96 % purity by HPLC.
Route of Synthesis
Project: CK05R

## Slide 9
Overview:
1.1 Kg of stage 6 compound is in hand with 98 % purity by HPLC.
100 g of stage 6 compound converted to stage 7 and got 71 g solid with 99.6 % purity by HPLC. (Yields: 87 %)
70 g of stage 7 compound converted to stage 8 and got 58 g with 98.4 % purity by HPLC. This was stirred with solvent (200 ml) at refluxing temperature, cooled to RT, filtered & dried got 51 g, its HPLC showed 99.6 %. (70 % yields)
500 g of stage 6 compound converted to stage 7 and got 351 g with 99.9 % purity by HPLC. (Yields: 86 %).
350 g of stage 7 compound converted to stage 8 and got 251 g with 99.6 % purity by HPLC
100 g of stage 6 compound converted to stage 7 and got 70.5 g, its HPLC showed 99 % purity.
70 g of stage 7 compound converted to stage 8 and got 46.8 g, its HPLC showed 99.7 % (Yield: 64 %)
50 g of stage 6 compound was attempted to convert to stage 7 and got 34.2 g solid with 99 % purity by HPLC (pH was adjusted to 8-9 using base solution).
34 g of stage 7 compound is being converted to stage 8.
Route of Synthesis
Project: A2NSQ

## Slide 10
Overview:
Attempted to treat 10 g of stage 7 compound with catalyst. After completion of the reaction, the mass was filtered and washed. Next, the compound was distilled. The filtrate and crude were dissolved in solvent and washed with acid. The acid layer was then washed with solvent twice and the acid layer pH had adjusted to 9-10 after the addition of a base. It was extracted with the solvent and distilled to produce 6.8 g of dark syrup. Its HPLC showed 80 % purity along with other un-known impurities, this crude product was treated with acid in solvent to produce a solid that was filtered, resulting in 2.5 g with 99.2 % HPLC (Yields: 24 %)
2 g of stage 7 compound was treated with catalyst at refluxing temperature, reaction was monitored by TLC, filtered the catalyst and RM was treated with acid but, the solid compound was not achieved.
Route of Synthesis
Project: A2NSQ

## Slide 11
Overview:
Raw materials ordered on 29-08-2026
Route of Synthesis
Project: BG5JD